## Slide 1: The event will begin momentarily.
This event is being recorded
Captions are available by clicking the CC icon in the Zoom toolbar below
ASL is provided
For more information and to download presentation materials visit: www.access-board.gov/av/

## Slide 2: Inclusive Design of Autonomous Vehicles: A Public Dialogue
Accessibility for Passengers with Mobility Disabilities: Part 1 Entering and Exiting Vehicles

## Slide 3: Agenda
Presentations
  U. S. Access Board – Randall Duchesneau
  University at Buffalo – Dr. Victor Paquet
  Q & A
  NMEDA – Amy Schoppman
  BraunAbility – Kevin Frayne
  Q & A
Open Dialogue
Dialogue continues online
  https://transportationinnovation.ideascale.com/
  PowerPoint slides available for download at:
  https://www.access-board.gov/av/

## Slide 4: How to Participate
Ask Questions to Presenters
  Submit questions using Zoom’s Q & A feature throughout the event
  Moderator will read question
  May not get to all questions
  Alternative : Email events@access-board.gov
Contribute to Open Discussion
  Request to speak using Zoom’s Q & A feature
    Ex. I’m Beth from XYZ Company and would like to talk about automated doors
    Ex. I’m Alex and I’d like to share my experience using an AV
  Host will enable your microphone
  Moderator will call on you to unmute and speak
  ASL – if you wish to be visible for signing, indicate in request
Online dialogue
  https://transportationinnovation.ideascale.com/
  For assistance, email: ePolicyWorks@dol.gov

## Slide 5: “inclusive design of autonomous vehicles”

## Slide 6: Existing Accessibility Guidelines
ADA Accessibility Guidelines for Transportation Vehicles (1991, 1998)
  https://www.access-board.gov/ada/vehicles/
Updated Guidelines for Buses and Vans (2016)
  https://www.access-board.gov/guidelines-standards/vehicles/update-buses-vans/guidelines-text/
  For technical assistance on these guidelines:
    800-872-2253 (v)
    800-993-2822 (tty)
    ta@access-board.gov

## Slide 7: U. S. Access Board: Accessibility Guidelines for Buses and Vans
Randall Duchesneau, Accessibility Specialist

## Slide 8: Technical Criteria
Entering and Exiting Vehicles
  At least one means of accessible boarding and alighting (ramps or bridge plates, lifts, level boarding)
  At least one means that can be deployed to the roadway
Walking Surfaces
Ramps and bridge plates
Slopes
Lifts
Level boarding
Steps
Doorways
Illumination

## Slide 9: Surfaces
Slip resistant
Openings
  5/8” sphere
  Perpendicular to dominant direction of travel
  Exception for wheelchair securement components and handles
Surface discontinuities
  ¼” vertical, ½” beveled at 1:2
  Steps

## Slide 10: Level Boarding
Coordinated to minimize the gap between the vehicle floor and boarding platform
Ramp needed if gap is greater than 2” horizontal or 5/8” vertical

## Slide 11: Ramps
Permitted to fold or telescope
Design load
  600 pounds if longer than 30”
  300 pounds if less than 30”
  (Placed at the centroid of the ramp distributed over an area of 26” x 26”)
When in use, firmly attached to the vehicle
When not in use, means of storage (i.e. compartment / securement system)
Capable of manual operation (in case of power failure)

## Slide 12: Ramp features
Clear width 30” wide (min.)
Edge guards
  2” high (min.) along each side to within first 3”
Visual contrast
  1” (min.) stripe along perimeter
  Light on dark, or dark on light
Slopes

## Slide 13: Lifts
Comply with NHTSA FMVSS:
  49 CFR 571.403 and 571.404
Designed to permit boarding facing toward or away from vehicle

## Slide 14: Doorways
Vertical clearance (min.)
  Finished edge of door opening to highest points of the deployed lift, ramp or bridge plate below
  Depends on size and type of vehicle
    Over-the-road buses – 65”
    Other vehicles < 25 feet – 56”
    Other vehicles > 25 feet – 68”
    [Buildings: 78” - 80”]
Clear width
  32“ min. for doorways with level boarding
Thresholds marked with 1“ stripe
Notes: Over-the-road bus means a bus characterized by an elevated passenger deck located over a baggage compartment.

## Slide 15: Illumination
Lights shielded (don’t project directly into eyes of passengers)
Required at ramps, bridgeplates, doorways
  2 foot-candles (22 lux) min.
Required at boarding and alighting areas (exterior illumination)
  3 feet (min.) beyond ramp/steps
  1 foot-candle (11 lux) min.

## Slide 16: Victor Paquet, ScD
Center for Inclusive Design and Environmental Access
University at Buffalo Department of Industrial and Systems Engineering

## Slide 17: Accessibility for Passengers with Mobility Disabilities: Part 1 Boarding and Exiting
Victor Paquet, ScD
U.S. Access Board Public Forum on Autonomous Vehicles

## Slide 18: Introduction
While ramps afford accessibility that stairs do not, all ramps are not created equal.
  Boarding and exiting public transit vehicles via ramps can be challenging.
Today’s presentation will summarize the results of two vehicle ramp studies:
  Study 1: Effects of ramp slope on human performance during ramp ascent and descent
  Study 2: Effects of multi-segment ramp configuration on human performance during boarding and exiting in a simulated vehicle environment
Some of the findings can be applied to public autonomous public transit (i.e., public self-driving vehicles).

## Slide 19: Study 1: Research Questions
What is the impact of ramp slope on the ramp ascent and descent performance of mobility aid users?
Does ramp slope have a differential effect on the performance of individuals who use different types of mobility aids?

## Slide 20: Study 1: Study Design (n=80)
Group | n | Age Range
Manual Wheelchair | 14 | 19-55
Power Wheelchair | 20 | 29-82
Scooters | 5 | 29-65
Cane/Service Animal (Visually Impaired) | 20 | 22-75
Other Walking Aid | 21 | 28-80
1:12
1:8
1:4
1:6

## Slide 21: Study 1: Ramp Ascent Time
ANOVA: Main effects for user group (p<.001) & slope (p=.027).

## Slide 22: Study 1: Ratings of Perceived Exertion for Ramp Ascent
ANOVA: Main effects for user group (p<.001) and slope (p<.001).
Hard
Somewhat Hard
Very light

## Slide 23: Study 1: Ratings of Perceived Difficulty for Ramp Ascent
ANOVA: Main effects for user group (p<.001) and slope (p<.001).
Very Easy
Very Neither
Very
Difficult

## Slide 24: Study 1: Other Findings
        Successful Use
        1:4 – 9 (33%) could not complete trial
        1:6 – 4 (14.8%) could not complete trial
        1:8 – 1 (3.7%) could not complete trial
        1:12 – all completed trial
        Usability
Power WC users, individuals with VI, and ambulation aids users rated descent more difficult than ascent at slopes of 1:4 and 1:6.
Some participants expressed concerns about using the ramp in winter.

## Slide 25: Study 2: Research Questions
Does the ramp deployment landing height for a multi-segment bus ramp affect user performance as users enter or exit the bus?
Do the slopes of a multi-segment bus ramp differentially affect users of different types of mobility aids?

## Slide 26: Study 2: Study Design (n=66)
Participant Group | n
Manual Wheelchair | 15
Power Wheelchair | 15
Scooter | 6
Cane/Service Animal (Vision Impaired) | 15
Walking Aid | 15

## Slide 27: Study 2: Test Conditions
Ramp Condition | Segment Angle (rise:run equivalent) |  | 
 | Inside | Middle | Outside
A. Below Street Level | 1.2° - | 9.0° (1:6.3) | 11.7° (1:4.8)
B. Street Level | 1.3° - | 8.9° (1:6.4) | 9.1° (1:6.2)
C. 3.5" Curb | 1.3° - | 2.5° - | 7.8° (1:7.3)
D. 4.5" Curb | 1.3° - | 0.4° - | 7.6° (1:7.5)
E. 6" Curb | 1.3° - | 0.3° - | 5.7° (1:9.9)
F. High Curb 8” | 1.3° - | 0.3° - | 3.6° (1:15.7)

## Slide 28: Study 2: Findings (Time)
Ascent
Descent

## Slide 29: Study 2: Findings (Difficulty Ramp Ascent)

## Slide 30: Study 2: Other Findings
20% of manual wheelchair users need assistance even on a 4.5 inch curb (steepest segment measures 1:7.5).
The challenging grade break conditions created with older (two-segment) ramps were alleviated by the three-segment ramp design.
Ramps should be designed to be at floor grade within the bus (i.e., do not cut into floor) to reduce trip and fall hazards and maximize clear spaces for turning and maneuvering.

## Slide 31: Research Implications for Self-Driving Vehicles
Our work supports a maximum slope for transit ramps of 1:6, with less severe slopes preferred to support independent ascent of manual wheelchair users.
With a 1:6 maximum condition at street level, any environmental facilitation will support easier entry and exit:
  Deploy ramp to curb wherever possible, and ideally at corners or sidewalks that have enough clear space.
  Standardize pick-up and drop-off conditions to allow loading to curb.

## Slide 32: Other Implications for Self-Driving Vehicles
Automatic door and ramp deployment needs to be addressed.
  Treat each passenger similarly
  Automate to passengers’ preferences
  Communicate deployment status to passenger
Appropriate ramp storage is challenging, but possible.
The pick-up and drop-off location ideally will be curb height but must have enough clearance to allow passengers to maneuver onto and off of the ramp easily.
  E.g., Avoid deploying halfway onto a narrow sidewalk

## Slide 33: Sponsor
This presentation was funded in part by grants from the National Institute on Disability, Independent Living, and Rehabilitation Research (NIDILRR) grant numbers H133E080019 and 90RE5011. NIDILRR is a Center within the Administration for Community Living (ACL), Department of Health and Human Services (HHS). The contents of this presentation do not necessarily represent the policy of NIDILRR, ACL, HHS, and you should not assume endorsement by the Federal Government.

## Slide 34: Questions/ Comments
Victor Paquet, Sc.D.
Center for Inclusive Design and Environmental Access
University at Buffalo, Department of Industrial and Systems Engineering
341 Bell Hall | Amherst, NY 14221
vpaquet@buffalo.edu

## Slide 35: Amy Schoppman
Director of Governmental Affairs
National Mobility Equipment Dealers Association
(NMEDA)

## Slide 36: National Mobility Equipment Dealers Association

## Slide 37: Kevin Frayne
Director of Advanced Mobility Solutions
BraunAbility

## Slide 38: Kevin Frayne, Director of Advanced Mobility Solutions

## Slide 39: Accessible Transportation Milestones
1966
Ralph Braun
1990
202x
AVs

## Slide 40: Topics
Accessible AVs: Evolution or Revolution?
A Geometry Refresher
Autonomous = Electric = Batteries?

## Slide 41: AVs: Evolution or Revolution?
Autonomous vehicles are: (a) like today’s vehicles; (b) reimagined transportation solutions; (c) electric; (d) privately owned; (e) shared; (f) multi-passenger public transportation; (g) all of the above.

## Slide 42: AVs: Are Everything
(g) all of the above – and should be accessible

## Slide 43: Entry / Exit = It’s All About the Geometry
Step-In: 10” / 250mm (or less) with kneeling is an “okay” place to be. 8” / 200mm is better.
Current ADA
1:4 / 14o Ramp
Proposed ADA
1:6 / 9.5o Ramp

## Slide 44: Step-In Height (w/kneeling) Drives the Solution
Lifts do not lend themselves as easily to full autonomous operation
Rarely do ramps and lifts compete for an application

## Slide 45: It’s All About the Geometry
Door Openings & Heights: Are greater than typically designed to for ambulatory usage
  A: Door Width: ADA = 32” min.
  B: Door Height: ADA = 56” min.
  C: Interior Height: 59-61” min.

## Slide 46: Batteries = New Challenges
Underfloor batteries constrain entry/exit solutions
  Sometimes structural, almost never moveable
  Have integrated liquid cooling systems and other complexities
  Precludes attaching lifts, ramps, and WC securement through the vehicle floor

## Slide 47: Batteries: Vehicle Accessibility Solutions
Go Above the Floor: On-floor fold-out ramp that attaches at the vehicle threshold.
Go On the Floor: Bonded (non-intrusive) flooring system that provides attachments for lifts, ramps, and WC securement solutions.
Go Below The Floor: 50mm slot (above batteries, below the floor) to accommodate an ultra-thin ADA ramp solution.
Evolutionary to Revolutionary Solutions

## Slide 48: Summary: AVs - An Accessibility Evolution and Revolution
Innovate for the Now and the Later
  100% automated vs. 100% accessible: Don’t wait for the first to do the second.
Step-In is Critical: New EV architectures will severely limit their ability to accommodate ramp solutions if this is ignored
AVs are EVs and have unique accessibility challenges (and solutions) due to batteries
Innovation

## Slide 49: BraunAbility Global Innovation Lab, Carmel, IN
Accelerate market-shaping innovation with a focus on EVs, AVs, sensing, IoT, etc.
Purdue Autonomous Vehicle Accessibility project will be based here
Opening April 1, 2021

## Slide 50: Questions?

## Slide 51: Open Discussion
Request to share information, ideas, or comments using Zoom’s Q & A feature:
  Name (and organization)
  Brief description of content
Host will enter you into queue
Moderator will announce when you should unmute (*6 by phone)
Moderator will also announce next in que
Presenters may respond to some comments
Alternative: events@access-board.gov
ASL – note in request to comment
Please limit comments to < 2 min.

## Slide 52: Online Dialogue
Continue the conversation Online
  https://transportationinnovation.ideascale.com/
  Share ideas, comment, vote
  For assistance, email: ePolicyWorks@dol.gov

## Slide 53: Next Session
Accessibility for Passengers with Mobility Disabilities: Part 2
This session will address maneuvering and securement in vehicles and continued discussion of entering and exiting autonomous vehicles.
March 24, 2021, 2:00 – 3:30 (ET)
Welcome remarks by Jennifer Sheehy, Deputy Assistant Secretary of Office of Disability Employment Policy, Department of Labor.
Presenters:
Scott Windley, U.S. Access Board
Bryan Brillhart, Robotics Research
Dr. Kathleen D. Klinich, University of Michigan
Dr. Jordana Maisal, University at Buffalo

## Slide 54: U.S. Access Board Meeting 4:00 – 5:00 ET
Executive Director’s Report
Standing & Ad Hoc Committee Reports
Election Assistance Commission
New Business